LAB 3 – WIRED TOPOLOGY IMPLEMENTATION

Overview

Objective is to implement a 3 source nodes to 1 destination node topology in NS2 using wired transmission medium.

Steps

1) Create a simulator object.
2) Define different colors for data flows (for NAM)
3) Define a 'finish' procedure
4) Create four nodes n0 n1 n2 and n3
5) Create links between the nodes
6) Set Queue Size of link (n2-n3) to 10
7) Give node position (for NAM)
8) Monitor the queue for link (n2-n3). (for NAM)
9) Setup a TCP connection
10) Setup a FTP over TCP connection
11) Setup a UDP connection
12) Setup a CBR over UDP connection
13) Schedule events for the CBR and FTP agents
14) Detach tcp and sink agents
15) Call the finish procedure after 5 seconds of simulation time
16) Print CBR packet size and interval
17) Run the simulation.

Key Commands

set - assigning values
proc - defining procedure
ns duplex-link - creates two simplex links of specified bandwidth and delay, and connects the two specified nodes
ns attach-agent - attaches an agent object created to a node object
tcp,cbr,ftp,udp - commands for setting up respective connections
puts - print OP

References

https://github.com/kvalli/NS2_Wired_Example