LAB 5 – CONGESTION CONTROL ALGORITHMS

Overview

Objective is to implement TCP Tahoe and TCP Reno.

Steps

TCP Tahoe:

Slow Start phase: It lasts until congestion window size reaches up to “Slow Start Threshold (ssthresh)“. The slow start algorithm doubles the congestion window size(cwnd) in one RTT. Initially, ssthresh is set to infinite(∞). Subsequently, it adapts depending on the packet loss events. When cwnd becomes equal to ssthresh, slow start stops

AIMD phase: It starts when the slow start stops. Additive Increase increases cwnd by 1 and Multiplicative Decrease reduces ssthresh to 50% of cwnd. Note that cwnd is ‘not’ reduced by 50% but ssthresh..

Fast Retransmit phase: It is the loss detection algorithm. It is triggered by 3 duplicate acknowledgments. On packet loss detection, it resets cwnd to initcwnd.

TCP Reno = TCP Tahoe + Fast Recovery

Fast Recovery Phase: It makes use of both RTO and Fast Retransmit. If the packet loss detection is triggered by 3 duplicate acknowledgments then it is a fast retransmit algorithm in action. On packet loss detection through Fast Retransmit, cwnd is reduced by 50% (cwnd = cwnd/2). 3 duplicate ACKs are received that means network is performing well because ACKs are being received which means packets are getting delivered to the receiver

Key Commands

set - assigning values
proc - defining procedure
ns duplex-link - creates two simplex links of specified bandwidth and delay, and connects the two specified nodes
ns attach-agent - attaches an agent object created to a node object
tracevar - allows a C procedure to monitor and control access to a Tcl variable, so that the C procedure is invoked whenever the variable is read or written
puts - print OP

References

https://github.com/basant-kumar/Computer_Networks_Lab/tree/master/TCP_protocols_simulator